## Slide 1
Fluid Control Components for Semiconductor Manufacturing
(Wet process)
Basic version
August 29, 2007 Rev.
CKD Corporation

## Slide 2: Fluid Control Components are
<number>
Like a water faucet, these components control fluid by
Stopping the flow
Running the flow
Adjusting the amount of flow
Faucet

## Slide 3: What is Fluid Control Components?
<number>
Usually faucets are opened and closed by hand.
However, Fluid Control Valves can be opened/closed automatically by a mechanism.
Imagine a water faucet with automated open/close…
＋
自動
I am a faucet.
I will not be opened unless manually operated.
Automated mechanism

## Slide 4: What is Fluid Control Components and its usage?
<number>
Vending machine
Carwash machine
Vending machines as the most widely used example, fluid control components are utilized where various fluids such as air, water, oil, and aqueous solution are controlled by ON/OFF, including industrial machines, machine tools, precision machines, water processors, washrooms, etc.

## Slide 5: Fluid control method for automation
<number>
Electric
Manual input
Pneumatic pressure method
Mechanical method
Electric method
ON/OFF and flow rate are controlled by Electromagnet, motor, etc.
ON/OFF and flow rate are controlled by pneumatic pressure.
ON/OFF and flow rate are manually controlled by human operators

## Slide 6: Use Conditions for Semiconductor Manufacturing
<number>
Fluid
  Process gas…flammable, corrosive, toxic, and pure
  Chemical…corrosive, toxic, and pure
  Pure water…pure
  Vacuum…corrosive, toxic, byproduct
  City water
Control
  Precision control…flow rate, pressure, temperature, repeatability
These fluid control components are more specialized due to their selective environment rather than general environment.
=> Components that are suitable for each system requirements are selected.

## Slide 7: Components for Chemical Used in Semiconductor and LCD Manufacturing
<number>
P
Regulator
Sensor
Flow rate
Pressure
Tank
Tank
P
Various device
Drainage equip.
Drainage equip.
Pump
Filter
Pump
Valve
Equip. for supplying fluid
Device
Valve
Valve
Valve
Others:
Piping and fitting
Acid
Alkali
Organic solvent
Pure water
etc.
Notes: <number>

## Slide 8: Mechanisms of Valve
<number>
Notes: <number>

## Slide 9: Air Operated Valve Structure
<number>
Actuator
is where pneumatic pressure is applied and the diaphragm is moved up and down to operate the valve open/close.
Diaphragm
separates fluid from the outside and causes valve to open/close per piston rod motion.
Fitting
is where piping is connected.
There are many kinds of fittings to accommodate your needs.
Valve seat
is where diaphragm gets engaged and the fluid is
intercepted.
Air operated type is most widely used in the semiconductor manufacturing.
Notes: <number>

## Slide 10: Actuator types and Valve actuations
<number>
NC type
(Normally close)
NO type
(Normally open)
Double action
Open operation
Close operation
AIR
AIR
AIR
AIR
Notes: <number>

## Slide 11: Component Features per Fluid ~ For Chemical ~
<number>
Notes: <number>

## Slide 12: Features of Component for Chemical
<number>
Typical fluororesin used for chemical contact area
PTFE (polytetrafluoroethylene resin)
=> Mainly for machining, white
PFA (Tetrafluoroethylene perfluoroalkoxy vinyl ether copolymer)
=> Mainly for molding, translucent
Main features why fluororesin is used for chemical
(Excerpt from Teflon practical handbook by DU PONT-MITSUI FLUOROCHEMICALS COMPANY,LTD)
  Chemical resistance…Inactive to most chemical
  => Safe to contact chemical
  Heatproof…maximum continuous operating pressure: 260˚
  Fusing point: PTFE…327˚C, PFA...305˚C
  => Withstand higher temperature compared to other resins.
  Purity…Chemically inactive and pure. Absolutely no additive is present.
  => Does not contaminate chemicals
Points to be noted when using components
  Deformation
  Penetration
  Compatibility with chemical
  Electro static charge
“Fluororesin” is widely used for fluid contact area of components for chemical.
Port B
Port A
Item | Part name | Material | Qty
1 | Actuator assembly | PPS | 1
2 | Body | PFA | 1
3 | Mounting plate | PPS | 1
4 | Diaphragm | PTFE | 1
Notes: <number>

## Slide 13: Fitting type
<number>
Inch Size 1/4”～1“
Metric Size 6～25
Super 300
Final Lock
Inch Size 1/4”～1“
Metric Size 6～25
Inch Size 1/4”～1“
Flaretek
Inch Size 1/4”～1“
Metric Size 3～25
20A Series
Inch Size 1/8”～1“
Metric Size 3～25
60 Series
Inch Size 1/8”～1“
Metric Size 3～25
Super Fitting
Various types supplied by fitting manufactures
Apply fittings according to the latest instruction manual issued by each fitting manufacturer.
Notes: <number>

## Slide 14: Air Operated Valves
<number>
With flow control
Stainless-steel body
May be selected for electrification prevention
Standard
With by-pass
residence in pure water line while valve is closed
By-pass: Normally open
Main: Open/close operations
Variations
Notes: <number>

## Slide 15: Manifold Valve
<number>
Pressurizing/opening to tank
Multi-distributing
2 Station manifold
Purpose:
Switching, multi-dropping, and merging chemicals
Pressurizing/opening toward tank
D.I.Water
Chemical A
Chemical B
Chemical A
N2
Exhaust
Replace the tank
Switching chemicals
Notes: <number>

## Slide 16: For Specific Applications
<number>
Application and developing process
  Improved control to react to fluid shortage
  Less foam
  Small flow control
Fluid supplying apparatus
  Improved replacement
  High pressure
  Less water hammer effect
Notes: <number>

## Slide 17: Improvement on fluid control
<number>
Diaphragm actuator
Standard type
Diaphragm actuator
Low sliding friction valve
Advantages of diaphragm actuator:
Frictional resistance of diaphragm actuator is less than that of the standard type, thus easier to control speed.
Speed controller
=> By adjusting the exhaust speed, valve closing speed can be controlled.
Purpose: Easier to adjust the exhaust speed and control the valve closing speed.
w/ flow rate control
Notes: <number>

## Slide 18: Less Foam
<number>
Foam control valve
Lower the cause of foam
Decrease pressure loss
Lower the impact when valve opens (water hammering)
Increased diameter of orifice
By increasing the diameter of orifice, decrease pressure loss.
Low sliding friction actuator
Speed controller controls the open/close speed and prevent sudden pressure change (water hammering).
Our standard item
Notes: <number>

## Slide 19: Small Flow Control
<number>
Small flow control valve
Existing flow rate control
Key features
Structure that less fluctuates flow rate
=>Functions of valve opening/closing and flow rate control are separated
Adjustable by fine pitch
=> Differential screw is used for flow rate control area
When it returns to normal, narrows the passage
=>flow rate fluctuates
Valve open/close area
Flow control area
Port B
Port A
Valve opens
Port B
Time passes
Comparison of flow rate characteristics
w/ flow rate control
Knob rotations
Flow rate
Fluid: water Differential pressure: 0.1MPa
Downward force of spring stops and release the diaphragm.
Notes: <number>

## Slide 20: Improved Replacement Time
<number>
0
18
Time (sec)
Resistance
Ratio [MΩ]
17.9MΩ
10.0MΩ
2.0 hrs
PAMD
Existing piping
Quick maintenance valve PAMD
Use point
Chemical supply
DIW
Reduce man-hour for
Replacing manifold
System piping cleaning
For high maintenance demand
Evaluation result on replacing
You can clean ‘out port’ while the valve is closed
Integrated purge port
Notes: <number>

## Slide 21: High Pressure
<number>
Able to supply high pressure (0.7MPa) – large flow rate (1.25inch)
Various fittings are available
  S300 type
  Flared type
  Piping for welding
Higher safety requirements along with higher pressure
  Improved valve seal
  Less water hammer
High pressure chemical supplying valve AMD H series
New Products
Notes: <number>

## Slide 22: Large Diameter
<number>
Key features
Large diameter of 1.5 inch
  Super 300 type Pillar fitting
  With 1.5 inch fittings
Air operated valves and manual
valves are available
Solution for large flow rate Cv
value 24
Large diameter chemical valve
New Products
Notes: <number>

## Slide 23: Less Water Hammer Effect
<number>
Our existing product
Less water hammer type
Water hammer relief valve AMD L series
New Products
Pressure (MPa)
Pressure (MPa)
Time after operating valve is turned off (sec.)
Time after operating valve is turned off (sec.)
Pressure In
Pressure Out
Pressure In
Pressure Out
Notes: <number>

## Slide 24: Other Fluid Components
<number>
Manual valve
Suck back valve
Regulator
  Manual
  Pilot type
Drainage valve
Fluid surface level switch
Notes: <number>

## Slide 25: Manual Valve
<number>
Screw-in type
Toggle type
Filter
Chemical
Manual valve
(Main- for maintenance)
Manual valve
(To filter foam)
Notes: <number>

## Slide 26: Suck Back Valve
<number>
Chemical
Air operated and suck back valve all in one type
Suck back valve
When the atmosphere goes through exhaust port, spring raises the diaphragm and capacity in the suck back valve increases, thus sucks up the fluid.
Purpose of installing suck back valve
Prevent fluid dropping on the wafer from nozzle-end that is positioned over the wafer
Exhaust
Air operated valve
Suck back valve
Notes: <number>

## Slide 27: Regulator
<number>
The purpose of regulator (pressure control valve)
  is to stabilize pressure fluctuations.
Types of regulator for chemical
Manual
Target pressure
Target pressure
Pilot type
Pressure
Time
Pressure
Time
Notes: <number>

## Slide 28: Manual Regulator
<number>
Fluid flow
The operation principle of regulator
1) Pressure at ‘out port’ increases
2) Raises the diaphragm
3) Narrows the passage
4) Force of pressure control spring
increases
=> Pressure at ‘out port’ decreases
Try to keep the pressure constant
1) Pressure at ‘out port’ decreases
2) Raises the diaphragm
3) The passage is widened
4) Force of pressure control spring decreases
=> Pressure at ‘out port’ increases
Upward force:
Force that diaphragm receives
Downward force:
Force of pressure control spring is
balanced.
Notes: <number>

## Slide 29: Pilot Type Regulator
<number>
Fluid
Pneumatic regulator
(manual or electro pneumatic)
Advantages of using the Pilot Regulator
Pressure can be remotely operated
Change set pressure/flow rate
Control flow rate to remain constant
=> Feedback control with pressure/flow rate sensor
New product launched in February 2007
Notes: <number>

## Slide 30: Drainage Valve
<number>
Plant drain line
Purpose:
Fast drain fluid inside the cleaning tank
=>Required large diameter, as drain the fluid by its own weight
Notes: <number>

## Slide 31: Fluid level Sensor
<number>
KML50 series
1 point type
Purpose:
To monitor the fluid level inside the cleaning tank
Advantage:
The sensor does not come in contact with the chemical solution.
=> Can be used to monitor/control the corrosive or penetration fluid level
KML60 · 70 series
Multipoint type
Accuracy ±1mm
Output point Point 1
±10mm Point 4/6
Cleaning tank
Cleaning tank
Inside tank
Outside tank
Upper limit
Lower limit
Over
Upper limit
Lower limit
Inside tank
Outside tank
Level 1
Level 2
Level 3
Level 4
Level 1
Level 2
Level 3
Level 4
Notes: <number>